## Slide 1: mux21_32 Standalone ChatGPT message
ChatGPT message
Create a mux21_32 VHDL model and testbench, with
input control signal sel (1-bit),
input 32-bit datapath signals muxIn1 and muxIn0,
output 32-bit signal muxOut.
If sel = 1, muxOut = muxIn1, else muxOut = muxIn0

## Slide 2: HDLGen and ChatGPT Digital Systems Design Capture Automation
Download, open HDLGen, select VHDL or Verilog generation, modify settings
Setup project folders and files
Capture design in HDLGen, from the design and test specifications
Generate files
  HDL model and testbench templates
  EDA project and simulation waveform configuration
Open EDA toolsuite, syntax check, simulate, synthesise
Generate ChatGPT file for HDL model and testbench completion
Run ChatGPT
  Generate complete HDL model
  Generate testbench HDL stimulus and output signal checking HDL.
  Paste in EDA tool
    HDL model template
    Testbench stimulus process
Simulate HDL (view and verify timing diagram and messages)
Synthesise logic (view schematics)

## Slide 3: 1. Download, open HDLGen, select VHDL or Verilog generation, modify settings
Download HDLGen https://github.com/fearghal1/HDLGen
Open HDLGen
Select VHDL or Verilog
Settings
  Creator details
  EDA tool link
  ChatGPT message header default

## Slide 4: 2. Setup project folders and files
Create
  Project name
  Project environment: folder for single or series of project
  Project folder, within the project environment
Download project
    Specification
    Test Plan (excel file)
    Specification text description file

## Slide 5: 3. Capture Design in HDLGen, from the design and test specifications
Component
VHDL-specific
  Signal Types
  Sub-components: add component to MainPackage VHDL package)
Ports
Internal signals
Architecture
Test Plan
ChatGPT message

## Slide 6: 4. Generate files
HDL model and testbench templates
EDA project
Simulation waveform configuration

## Slide 7: 5. Open EDA toolsuite, syntax check, simulate, synthesise
G

## Slide 8: 6. Generate ChatGPT files for HDL model and testbench completion
G?? enerate complete HDL model
Generate testbench HDL stimulus and output signal checking HDL.
Paste in EDA tool
  HDL model template
  Testbench stimulus process

## Slide 9: 7. Run ChatGPT
Generate complete HDL model
Generate testbench HDL stimulus and output signal checking HDL.
Paste in EDA tool
  HDL model template
  Testbench stimulus process

## Slide 10: 8. Simulate HDL
Simulate
View and verify timing diagram and messages

## Slide 11: 9. Synthesise logic (view schematics)
Simulate
View and verify timing diagram and messages